## Slide 1: Iot Vibration Sensor For Washing Machine
Angel Solis

## Slide 2: Goal
Main Goal
  The goal was to create an embedded application to inform the user when the laundry was done.
Objectives
  This goal was accomplished by interfacing a vaibration sensor with the NodeMCU(esp8266) which would then transmit the data to the BeagleBone Black.

## Slide 3: Outcome - Accomplishments
Outcome
  The vibration sensor detects when the washer is running by emitting a voltage to the NodeMCU
  The NodeMCU uses an ADC to convert the value from the vibration sensor to determine when the machine has stopped. Then the message “wash” is sent to the BeagleBone
  The BeagleBone looks for a message containing “wash” though the MQTT broker mosquitto. When the message is received an email is sent to the user.
  Short-term usefulness of this project is reminding the users when the washer is done.
  Long-term usefulness would be adding another node to inform when the dryer is also done.

## Slide 4: Components Used in Design
Grove - Piezo Vibration Sensor [1]
NodeMCU [2]

## Slide 5: Tools used in Design
Bash scripts [3]
Arduino IDE [2]
MQTT: Mosquitto [4]

## Slide 6: Schematics

## Slide 7: Pre-requisites used in Design
Prerequisites
Arduino IDE with NodeMCU & MQTT
BBB with MQTT
Commands to install MQTT on BBB
  $ vi /etc/apt/sources.list
    add deb http://httpredir.debian.org/debian stretch main contrib non-free
  apt-get update
  apt-get install mosquitto
  apt-get install mosquitto-clients
  $ vi /etc/apt/sources.list remove added deb

## Slide 8: Pre-requisites used in Design
Commands to edit conf file for MQTT
  In /etc/mosquitto/mosquitto.conf add
    allow_anonymous true
    listener port 1883
Commands to install MQTT on Arduino
  In Arduino package manager install
    ESP8266 HttpClient
    ESP8266 WiFi
    Adafruit MQTT Library
    PubSubClient

## Slide 9: Implementation Details
Knowing when washer is done:
  NodeMCU periodically checks to see if ADC value is over 50 and until keep checking.
  When ADC value is over 50 periodically check back to see when the machine has stopped.
  When it has stopped Publish a message though MQTT
      client.setServer(HOST, PORT);
      client.connect("ESP8266Client")
      if(client.loop())
      client.publish(topic, "wash", true);

## Slide 10: Implementation Details
Receiving the MQTT message (bashscript):
  Continuosly check for message containing “wash” Then Email the users.
      #!/bin/bash
      while :
      do
      if mosquitto_sub -t wash -C 2 | grep "wash"; then
      echo "Wash"
      cat wash.txt | sendmail -t
      fi
      done

## Slide 11: Actual project set-up
Screenshot of the project will all components

## Slide 12: Demo
https://youtu.be/yWMe8QvAheA

## Slide 13: Results and Conclusions
Fig[1]
Example output from NodeMCU
Fig[2]
Example output from BeagleBone
Fig[3]
Example email

## Slide 14: Reference
Grove – Piezo Vibration Sensor
Programming NodeMCU Using Arduino
Bash scripting tutorial
mqtt with BBB and NodeMCU